## Slide 1: Cavitating Venturi
REP 1 CDR Jack Igoe
Notes: 7 minute presentation, ITAR information redacted

## Slide 2: Project Overview
Problem:
Getting propellant into the engine according to propulsion’s requirements
  Mass flow rate can be passively regulated with a cavitating venturi
Function:
Decrease throat area to reach vapor pressure and cause cavitation
  Cavitation bubbles block the throat and restrict the flow
Difficulties:
Uncertainties
  Propulsion error tolerance, operating states, transient conditions
Notes: Difficulties: passive regulation sensitive to design changes – biggest challenge related to project
Transient conds: also steady state pressure fluctuations within control loop tolerance

## Slide 3: Sizing Calculator
Cd and pressure recovery given by manufacturer
Choose design inputs
Initial pressure sensitivity calculations

## Slide 4: Analysis
MATLAB script
Input temperature and pressure ranges, design inputs
Temperature  vapor pressure (equations pulled from NIST)
Pressure  affects dP

## Slide 5: Results Mass flow rate as a function of temperature with incremented pressure values
Notes: T_range = ITAR
P_range = ITAR

## Slide 6: Conclusion
Next Steps
Integrate REFPROP, apply density changes
Cryogenic shrinkage at throat
GFSSP sim
Tests
Things I learned
Engine tolerances are complex
Modularity is the most important goal for this kind of project
Notes: Modularity: because it’s passive control, small design changes or improved data completely change things. Engine is guaranteed to change-- matter of when and how much, not if